## Slide 1: ADD5211 4.5-40V, 88 LED Boost IC (200mA/LED)
Key Features
White LED driver based on inductive boost controller
  Wide input voltage range : 4.5V to 40V
  Adaptive output voltage to minimize power dissipation
  200kHz to 1.2MHz adjustable operating frequency
  Programmable UVLO
  Programmable soft start time for boost converter
  Programmable external MOSFET switching rising time
  Can power up to 88LEDs (4 strings of 22)
Drives up to four LED current sources with internal MOSFET
  Brightness control with PWM input
  LED current control from 40mA up to 200mA
  Up to 25kHz LED dimming frequency
  Analog current reduction with ISET pin
  1000:1 PWM dimming control at 300Hz
  ±1.5% String to String current matching
  ±3.0% Absolute current accuracy
General
  Open drain fault indicator
  LED open and LED short fault protection
  Thermal shutdown
  Under voltage lockout
  24-lead, 4mm X 4mm LFCSP package
Input Voltage
4.5V - 40V
Output Current
200mA/String (800mA total)
Output Voltage Range
~90V (max)
Status
Production

## Slide 2: ADD5211 Evaluation Board (Rev4):
Board Instructions
  Attach the ADD5211 eval board and LED board together.
  Adjust the jumpers on the LED board to choose the number of LEDs to drive.
  Connect:
    Vin to a supply between 8V and 36V
    PWM to a frequency generator
      Or, if PWM dimming is not required, connect PWM to the ADD5211’s VDD pin (default jumper connection).

## Slide 3
The first jumper in each row of LEDs shorts out 1 LED.
The other jumpers in each row short out 2 LEDs
Jumper Open : LEDs will be used
Jumper Short : LEDs will not be used
With all jumpers open, the LED voltage is about 62V per string at 100mA.
ADD5211 LED Board
LED Board can be plugged in “upside down” to make testing easier.

## Slide 4: ADD5211 Eval Board Layout (Rev 4)
Demo Board Layout: Top Metal
Default Jumper
Placement shown
with blue boxes

## Slide 5: ADD5211 Eval Board Bill of Materials (BOM)

## Slide 6: ADD5211 LED Board Layout (Rev 2)
(all LED cathodes face left)
Default jumper placement shown with red boxes

## Slide 7: ADD5211 Eval Board Ordering Info:
ADD5211CP-EVALZ =
ADD5211EB-EVALZ =
Order ADD5211CP-EVALZ to get the ADD5211 eval board and the LED board.
Order ADD5211EB-EVALZ to get just the ADD5211 eval (driver) board.
Then connect it to your own LEDs.